(Abstract) Improved Geo-location Accuracy for POES Imagery

POES imagery includes spacecraft time information, which is used during ground processing to geolocate image pixels.  Because POES spacecraft have no internal means to “know” what time it is, the NOAA /NESDIS Office of Satellite Operations (OSO)  routinely measures the difference between the spacecraft time and a true timing reference, called a “clock delta”.  Beginning with the launch of the first KLM-series satellite in 1998, users noticed a significant discrepancy between the clock deltas generated by their image navigation software and  OSO-calculated values. Resolution of this discrepancy required a rigorous systems engineering effort conducted by OSO, the NOAA/NESDIS Office of Systems Development (OSD), and NASA to determine the root causes and correct them.  The corrections included improvements to flight software, ground system hardware, and engineering processes.  As a result of these improvements, OSO is now able to consistently maintain the clock deltas on operational POES spacecraft to within ( 75 milliseconds of a true timing reference provided by the Global Positioning System (GPS).  This presentation describes the original problem and its root causes as well as the improvements made and their positive impact  to users of POES data.

Cynthia L. Hampton

Cynthia L. Hampton is the Chief of the Engineering Branch for NOAA/NESDIS Office of  Satellite Operations (OSO).  Her experience includes satellite engineering and mission operations for GOES, POES and DMSP satellite constellations.  She worked for 10 years as a civilian for the United States Air Force with experience in program planning and space launch operations.  Her area of expertise is in system engineering and project management.   Cynthia holds a BS in Electrical Engineering from The University of Alabama and a BS in Atmospheric Sciences from Purdue University.  She can be contacted at Cynthia.Hampton@noaa.gov.

# James Valenti

James M. (Jim) Valenti was born and raised in Pittsburgh, PA. He is currently the Mission Operations Manager for the National Polar-orbiting Operational Environmental Satellite Program (NPOESS).   He served over 10 years in the US Air Force, primarily with the Defense Meteorological Satellite Program (DMSP), where he worked as satellite operator, operations control center supervisor, and payload engineer.  He also worked for several years as a Program Manager for the US Nuclear Detonation Detection Program's ground segment.  After leaving the Air Force, Mr. Valenti worked for NOAA/NESDIS Office of Satellite Operations (OSO) as the Engineering Team Lead for the POES Program, and oversaw the launch on NOAA-17, one of the most successful launches in the program's history.  He received a BS in Aerospace Engineering from Penn State University in 1990 and an MS in Space Operations from the Air Force Institute of Technology in 1997.  He can be contacted at James.Valenti@noaa.gov.

# Peter Phillips

Peter W. Phillips is a Senior Project Engineer for The Aerospace Corporation, providing systems engineering support to the NOAA/NESDIS Office of Systems Development (OSD) and Office of Satellite Operations (OSO).  He has extensive experience in the POES and DMSP satellite programs, and his areas of expertise include satellite and ground timing, flight software, and statistical analysis.  Pete holds a BS in Aerospace Engineering and an MS in Industrial Engineering and Operations Research from Penn State University, and an MS in Management from Troy State University.  He can be contacted at Peter.Phillips@aero.org.