### GOES-12/N/O/P Imagers

### Timothy J. Schmit

NOAA/NESDIS, Office of Research and Applications, Advanced Satellite Products Team (ASPT)

The latest satellite in the operational GOES series, GOES-12, was launched on 23 July 2001. It achieved geostationary orbit on 12 August 2001. There was a six-week check-out period in the fall of 2001. Current plans are for this satellite to become operational (at the East position) during Spring 2003. The Imager on GOES-12 has been modified from the previous four imagers in this series. One change is the addition of a spectral band centered at 13.3 (m (at 8 km). The GOES-12 Imager also includes a spectrally modified 6.5 (m band with an improved spatial resolution from 8 km to 4 km at the sub-satellite point. The addition of the 13.3 (m band comes at the expense of eliminating the 12 (m band on the GOES-12/N/O/P Imagers. A 12 (m band will remain available on the GOES-12 and beyond Sounders, although with coarser spatial and temporal resolutions and less geographic coverage than is available with the GOES Imagers. The 12 (m band will be re-introduced on the next series of Imagers, slated to begin with GOES-R in approximately 2012.

Beginning with GOES-N, the imager data outages associated with eclipses and Keep-Out Zones will be significantly reduced, due to the addition of an on-board battery. The 13.3 (m band will also be at 4 km resolution beginning with GOES-O.

Timothy J. Schmit

Timothy J. Schmit works for the Advanced Satellite Products Team within the NESDIS Office of Research and Applications located in Madison, WI. Tim’s experience with satellite data includes deriving VAS temperature and moisture retrievals, and gradient winds with GOES-6/7, simulating the expected signal from the GOES-I (-8) Imager and Sounder instruments, instrument calibration and inter-calibrations, deriving meteorological products from both the current sounder and imager, involvement in data assimilation of Sounder products within numerical prediction models, and helping to prepare for the next generation geostationary imagers (Advanced Baseline Imager) and sounders (Advanced Baseline Sounder). Tim received his Bachelors (1985) and Masters (1987) degrees from the University of Wisconsin-Madison.