Prepared by NOAA

Agenda Item: N/A

Discussed in N/A

# NOAA Table of Satellites

# Current Polar-Orbiting Satellites Coordinated within CGMS

( as of 01 September 2009)

| Orbit type (equatorial crossing times) | Satellites in orbit (+operation mode) P=Pre-operational Op=operational B=back-up L=limited availability | Operator | Crossing Time A=Northw D=Southw +Altitude | Launch date | Status |
| --- | --- | --- | --- | --- | --- |
| Sun-synchr. “Morning” (6:00 – 12:00) (18:00 – 24:00) | NOAA-17 (B) | NOAA | 9:22 (D) 810 km | 6/02 | Functional. 10/28/2003 – AMSU-A1 Failed. 2/15/2003 – DTR5 Failed. 2/14/2008 – STX3 output power degraded to inoperable level. STX1 diminished performance. |
|  | NOAA-15 (B) | NOAA | 4:46 (D) 807 km | 05/98 | Functional (intermittent problems with AVHRR, AMSU-B & HIRS) AMSU-A1 channels 11 & 14 inoperative. |
|  | DMSP-F16 (Op) | NOAA | 20:04 (A) 850 km | 10/03 | Defense satellite. SSMIS. Data available to civilian users through NOAA. |
|  | DMSP-F15 (B) | NOAA | 19:37 (A) 850 km | 12/99 | Defense satellite. SSMT2 (microwave water vapor sounder) non-functional. Data available to civilian users through NOAA. |
|  | DMSP-F14 (B) | NOAA | 17:24 (A) 852 km | 04/97 | Defense satellite. SSMI (microwave imager), SSMT1 (microwave temperature sounder) non-functional and SSMT2 non-functional. No functional onboard recorder. |
|  | DMSP-F12 (L) | NOAA | 15:35 (A) 850 km | 8/94 | Defense Satellite. Satellite decommissioned on 10/12/08 |

| Sun-synchr. “Afternoon” (12:00 –16:00) (00:00 – 04:00) | NOAA-19 (Op) | NOAA | 13:51 (A) 870 km | 2/09 | Functional. Noise on MHS Channels H3 and H4 |
| --- | --- | --- | --- | --- | --- |
|  | NOAA-18 (B) | NOAA | 13:45 (A) 854 km | 5/05 | Functional. Noise on HIRS long wave channels. SBUV chopper motor intermittent seizures self-corrected via macros. 6/7/2009 – MIMU-2 failure (loss of redundancy). |
|  | NOAA-16 (B) | NOAA | 17:57 (A) 849 km | 09/00 | Functional, no APT. Intermittent problems with AVHRR. |
| Sun-synchr. “Early morning” ( 4:00 - 6:00) (16:00 – 18:00) | DMSP-F13 (B) | NOAA | 18:33 (A) 850 km | 03/95 | Defense satellite. Data available to civilian users through NOAA. Only 1 recorder on-board with limited functionality. |
|  | DMSP-F17 (Op) | NOAA | 17:31 (A) 850 km | 11/07 | Defense satellite. SSMIS. Data available to civilian users through NOAA. |

# Current Geostationary Satellites Coordinated within CGMS

(as of September 2009)

| Sector | Satellites currently in orbit (+type) P: Pre-operational Op: Operational B: Back-up L: Limited availability | Operator | Loca- Tion | Launch date | Status |
| --- | --- | --- | --- | --- | --- |
| WEST -pacific (180°W-108°W) | GOES-11 (Op) | NOAA | 135°W | 05/00 | X-Ray Positioner Failed 2/10/2008 |
| EAST-atlantic (108°W-36°W) | GOES-12 (Op) | NOAA | 75°W | 7/ 01 | SXI Imaging Indefinitely Suspended 4/12/2007 X-Ray Positioner Failed 4/12/2007 |
|  | GOES-10 (B) | NOAA | 60°W | 04/97 | Supports South America. Inverted, solar array anomaly, DCP interrogator on back-up. Decommissioning planned for 12/2009. |
|  | GOES-13 (B) | NOAA | 105°W | 5/16/2006 | In storage Mode XRS/EUV instrument had a capacitor failure rendering unit inoperable. |
|  | GOES-14 (P) | NOAA | 89.5°W | 6/27/2009 | In PLT |

# FUture Polar-Orbiting Satellites Coordinated within CGMS

(as of 01 September 2009)

| Orbit type (equatorial crossing times) | Future Additional Satellites | Operator | Planned launch date | Other information |
| --- | --- | --- | --- | --- |
| Sun-synchr. “Morning” (6:00 – 12:00) (18:00 – 24:00) |  |  |  |  |
|  | DMSP F-18 | NOAA | 10/18/09 | (SSMI/S) |
|  | DMSP F-20 | NOAA | 2014 | (SSMI/S) |
| Sun-synchr. “Afternoon” (12:00 – 16:00) (00:00 – 04:00) |  |  |  |  |
|  | NPP – NPOESS Preparatory Project | NOAA/NASA | 01/2011 | (833 km) (13:30 A) (VIIRS, CrIS, ATMS, OMPS, CERES) HRD |
|  | NPOESS-1 | NOAA | 03/2014 | (833 km) (13:30 A) LRD(AHRPT), HRD |
|  | NPOESS-3 | NOAA | 2020 | (833 km) (13:30 A) LRD(AHRPT), HRD |
| Sun-synchr. “Early morning” ( 4:00 - 6:00) (16:00 – 18:00) |  |  |  |  |
|  | DMSP-F19 | NOAA | 2012 | (SSMI/S) |
|  | NPOESS-2 | NOAA | 05/2016 | (833 km) (5:30 D) LRD(AHRPT), HRD |
|  | NPOESS-4 | NOAA | 2022 | (833 km) (5:30 D) LRD(AHRPT), HRD |

# Future Geostationary Satellites Coordinated within CGMS

# (as of 01 September 2009)

| Sector | Future additional satellites | Operator | Planned launch | (Planned location) Other remarks |
| --- | --- | --- | --- | --- |
| East Pacific (180°W-108°W) and West- Atlantic (108°W-36°W) | GOES-P | USA/NOAA | 04/2010 | 135° W or 75° W |
|  | GOES-R | USA/NOAA | 2015 | 135° W or 75° W |