## Slide 1
GOES-18 ABI L2+ LAP Products Provisional PS-PVR
October 12, 2022
Tim Schmit
GOES-R AWG
NOAA/NESDIS/STAR
GOES-R AWG LAP team: Zhenglong Li,
Jinlong Li
Richard Dworak,
UW-CIMSS
v1.4

## Slide 2: Agenda
Provisional Validation Product Maturity Assessment
  Data since June 22, 2022
Path to Full Maturity Review
Summary and Recommendations
The GOES-18 LAP achieved Beta on 5/11/2022

## Slide 3: Products Overview
Same as GOES-16 and 17, the GOES-18 ABI L2 LAP algorithm includes regression and physical retrieval based on the infrared spectral bands as input. The algorithm is applied to 5x5 ABI pixels (~10 km) for generating LAP products over clear sky. The LAP products include LVT, LVM, TPW, and DSI.
Band Number | Wavelength (µm) | Purpose
8 | 6.19 | High-level atmospheric water vapor, winds, rainfall
9 | 6.93 | Mid-level atmospheric water vapor, winds, rainfall
10 | 7.34 | Lower-level atmospheric water vapor, winds, and SO2
12 | 9.61* | Total ozone
13 | 10.33 | Surface and cloud
14 | 11.20 | Imagery, SST, clouds, rainfall
15 | 12.30 | Total water, ash, SST
16 | 13.30 | Air temperature, cloud heights and amounts
LAP products
Legacy Vertical Temperature profile (LVT)
Legacy Vertical Moisture profile (LVM)
Total Precipitable Water (TPW)
Derived Stability Indices (DSI)
              Lifted Index (LI)
              Convective Available Potential Energy (CAPE)
              Showalter Index (SI)
              K-Index (KI)
              Total Totals (TT)
9.61* : used only in regression step
Notes: * Only used in the regression step.

## Slide 4: Review: Time-Line/Context
01 Mar 2022 GOES-T Launch
14 Mar 2022 GEO orbit attained (GOES-18 at 89.5W)
16 May - ~ 6 Jun 2022 Spacecraft drift to 136.8W from 89.5W
7 Jun 2022 Post Launch Product Test (PLPT) begins
5 Jul - ~ 21 Jul 2022 Spacecraft nudge to 137.0W
~3 Jan 2023 Transition to operations (West satellite)

## Slide 5: PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_TPW06 | Quantitative analysis of M6 FD TPW | 100 | Complete | AWG
ABI-CONUS_TPW07 | Quantitative analysis of M6 CONUS TPW | 100 | Complete | AWG
ABI-MESO_TPW08 | Quantitative analysis of M6 Meso TPW | 100 | Complete | AWG
See RIMP for ABI L2+ Total Precipitable Water
Notes: PRO is responsible for 01 – 05.

## Slide 6: PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LVT06 | Quantitative analysis of M6 FD LVT | 100 | Complete | AWG
ABI-CONUS_LVT07 | Quantitative analysis of M6 CONUS LVT | 100 | Complete | AWG
ABI-MESO_LVT08 | Quantitative analysis of M6 Meso LVT | 100 | Complete | AWG
See RIMP for ABI L2+ Legacy Vertical Temperature Profile
Notes: PRO is responsible for 01 – 05.

## Slide 7: PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_LVM06 | Quantitative analysis of M6 FD LVM | 100 | Complete | AWG
ABI-CONUS_LVM07 | Quantitative analysis of M6 CONUS LVM | 100 | Complete | AWG
ABI-MESO_LVM08 | Quantitative analysis of M6 Meso LVM | 100 | Complete | AWG
See RIMP for ABI L2+ Legacy Vertical Moisture Profile
Notes: PRO is responsible for 01 – 05.

## Slide 8: PLPTs Under Review
PLPT ID | Descriptive Title | % Complete | Results | AWG POC
ABI-FD_DSI06 | Quantitative analysis of M6 FD DSI | 100 | Complete | AWG
ABI-CONUS_DSI07 | Quantitative analysis of M6 CONUS DSI | 100 | Complete | AWG
ABI-MESO_DSI08 | Quantitative analysis of M6 Meso DSI | 100 | Complete | AWG
See RIMP for ABI L2+ Derived Stability Indices
Notes: PRO is responsible for 01 – 05.

## Slide 9: PLPT Tests for each Domain
Analysis Method | FD | CONUS | MESO
Visual Inspection |  |  | 
Comparison to reference data (RAOB, GPS, AMSR2) |  |  | 
Our 3 PLPTs dealing with analysis are comprised of the same 2 methods.
Each contains the applications of these methods on the FD, CONUS and MESO domains.
The applications of each method to each domain is summarized below.
Some methods were redundant or not possible for some domains.
Same as what was done for GOES-16/17 LAP

## Slide 10: Provisional Validation Product Maturity Assessment
GOES-18 ABI L2+ LAP Products Provisional PS-PVR

## Slide 11: GOES-18 Data Used in this Review
July 2022 - September 2022:
All FD, CONUS, Meso1, and Meso2 LAP with RAOB, Suomi-Net GPS TPW, and AMSR2 TPW matchups within +/- 30 min, 20 km
September 1, 2022, 0000 UTC: Visual images of all domains for each variable;
September 15, 2022, 0000 UTC:
  GOES-18 and GOES-16 intercomparison
October 5, 2022, 0000 UTC:
  GOES-18 and GOES-17 intercomparison
September 25, 2022, 1700 UTC – 2100 UTC:
  M4 mode test (5 min. full disk data);
August 14, 2022, 0100 UTC – 0650 UTC:
  Sun migration effect on produtc
11

## Slide 12: Definitions of Metrics
Passed: No visual artifacts and/or the comparison with the reference data near or above the specification.
Failed: Cause of performance degradation is unknown.
The comparisons with the reference data are computed over all data.
12

## Slide 13: Examples of Visual Inspection of All Domains
13

## Slide 14: PLPT ABI-FD-TPW, LVT, LVM:
TPW (mm)
Temp (K). 500 hPa
WV (g/kg) 850 hPa
14
TPW: Total Precipitable Water
LVT: Legacy Vertical Temperature profile
LVM: Legacy Vertical Moisture profile
September 01 2022, 0000 UTC

## Slide 15: PLPT ABI-FD-DSI:
15
LI: Lifted Index
CAPE: Convective Available Potential Energy
TT: Total Totals
KI: K-Index
SI: Showalter Index
September 01 2022, 0000 UTC
LI
CAPE
TT
KI
SI

## Slide 16: PLPT ABI-CONUS-TPW, LVT, LVM:
TPW (mm)
Temp (K). 500 hPa
WV (g/kg) 850 hPa
16
TPW: Total Precipitable Water
LVT: Legacy Vertical Temperature profile
LVM: Legacy Vertical Moisture profile
September 01 2022, 0000 UTC

## Slide 17: PLPT ABI-CONUS-DSI:
17
LI: Lifted Index
CAPE: Convective Available Potential Energy
TT: Total Totals
KI: K-Index
SI: Showalter Index
September 01 2022, 0000 UTC
LI
CAPE
TT
KI
SI

## Slide 18: Locations of Suomi-Net GPS and RAOB
Suomi-Net GPS
RAOB
18
Notes: On the left figure, all the red dots indicate SuomiNet-GPS locations and the blue dot in Dominican Republic (lat: 18.79, lon: -70.66) indicates the location
where most of the outliers in tpw figures are located.
On the right figure, all the red dots indicate RAOB locations and the blue dot near the Michigan Lake (lat: 43.75, lon: -87.71) indicates AERI observation.

## Slide 19: Comparison TPW with the GPS, RAOB, AMSR2
19

## Slide 20: Requirements for ABI LAP product: TPW
20
Product |  | Accuracy | Precision | Range
Temperature |  | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture |  | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | 0 - 100%
TPW |  | 1 mm | 3 mm | 0 - 100 mm
DSI | LI | 2.0 K | 6.5 K | -10 ~ 40 K or above
 | CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
 | SI | 2.0 K | 6.5 K | -10 ~ 4 K or above
 | TT | 1 K | 4 K | -43 ~ 56 K
 | KI | 2 K | 5 K | 0 - 40 K

## Slide 21: PLPT ABI-FD-TPW vs GPS:
2022.07-2022.09
21
number: 454892
bias: 0.04 mm
std: 2.97 mm
rmse: 2.97
Accuracy spec: 1 mm
Precision spec: 3 mm
PASSED
number: 484987
bias: -0.08 mm
std: 3.00 mm
rmse: 3.00
number: 290637
bias: -0.45 mm
std: 2.83 mm
rmse: 2.87
July August September
STD
BIAS
RMSE

## Slide 22: PLPT ABI-CONUS-TPW vs GPS:
2022.07-2022.09
22
number: 243681
bias: -0.41 mm
std: 2.77 mm
rmse: 2.80
Accuracy spec: 1 mm
Precision spec: 3 mm
PASSED
number: 269676
bias: -0.58 mm
std: 2.99 mm
rmse: 3.05
number: 102347
bias: -1.06 mm
std: 2.82 mm
rmse: 3.01
July August September
STD
BIAS
RMSE

## Slide 23: PLPT ABI-FD-TPW vs RAOB:
2022.07-2022.09
23
Accuracy spec: 1 mm
Precision spec: 3 mm
number: 1788
bias: -0.79 mm
std: 3.01 mm
number: 1013
bias: -1.01 mm
std: 3.19 mm
number: 400
bias: -0.77 mm
std: 2.68 mm
July August September

## Slide 24: PLPT ABI-FD-TPW vs AMSR2:
2022.07-2022.09
24
Accuracy spec: 1 mm
Precision spec: 3 mm
PASSED
number: 517779
bias: -0.62mm
std: 2.46 mm
number: 678006
bias: -0.71 mm
std: 2.52 mm
number: 535477
bias: -0.67 mm
std: 2.427 mm
July August September
STD
BIAS
RMSE

## Slide 25: TPW Performance Summary
TPW retrieval is working as expected on GOES-18 ABI data when combined with NWP short-rang forecasts (as first guess);
With a quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB, AMSR2, GPS, overall it does indicate performances meet spec. for all the coverages (FD, CONUS, Meso1, and Meso2), except in August the value compared with RAOB is a bit larger.

## Slide 26
Real-time GOES-18 ABI LAP product validation webpage soundingval.ssec.wisc.edu
Imagery (Fulldisk TPW)
Regional Plots with GPS
Station TPW Plots

## Slide 27: Comparison LVT & LVM with the RAOB
27

## Slide 28: Requirements for ABI LAP products: LVT, LVM
28
Product |  | Accuracy | Precision | Range
Temperature (LVT) |  | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture (LVM) |  | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | 0 - 100%
TPW |  | 1 mm | 3 mm | 0 - 100 mm
DSI | LI | 2.0 K | 6.5 K | -10 ~ 40 K or above
 | CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
 | SI | 2.0 K | 6.5 K | -10 ~ 4 K or above
 | TT | 1 K | 4 K | -43 ~ 56 K
 | KI | 2 K | 5 K | 0 - 40 K

## Slide 29: PLPT ABI-LVT, LVM (vs RAOB):
2022.07-2022.09
29
LVT (K)
LVM (%)
Full Disk
CONUS
Meso1
Accuracy spec:
1 K (BL-400hPa)
Precision spec:
2 K (BL-400hPa)
Accuracy & Precision spec:
18% (sfc-300hPa), 20% (300-100hPa)
Notes: Full disk has large STD possibly due to lower RAOB quality from non-USA countries. MESO might not have enough samples for statistics.

## Slide 30: LVT and LVM Performance Summary
LVT and LVM retrievals are working as expected on GOES-18 ABI data when combined with NWP short-range forecasts (as first guess);
Retrievals are sensitive to first guess;
With a highly quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB, the performances overall meet spec. for all the coverages (FD, CONUS, Meso1, Meso2), except for the near surface temperature, and also for the Relative Humidity at upper troposphere (100 - 300 hPa) when compared with RAOB, which is likely due to the known issue of dry bias of radiosonde observations.
30

## Slide 31: Comparison DSI with the RAOB
31

## Slide 32: Requirements for ABI LAP products: DSI
32
Product |  | Accuracy | Precision | Range
Temperature |  | 1 K below 400 hPa and above boundary layer | 2 K below 400 hPa and above boundary layer | 180 - 320 K
Moisture |  | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | Sfc - 300 hPa: 18% 300 - 100 hPa: 20% | 0 - 100%
TPW |  | 1 mm | 3 mm | 0 - 100 mm
DSI | LI | 2.0 K | 6.5 K | -10 ~ 40 K or above
 | CAPE | 1000 J/kg | 2500 J/kg | 0 - 5000 J/kg
 | SI | 2.0 K | 6.5 K | -10 ~ 4 K or above
 | TT | 1 K | 4 K | -43 ~ 56 K
 | KI | 2 K | 5 K | 0 - 40 K

## Slide 33: PLPT ABI-FD-DSI:
2022.07-2022.09
LI vs RAOB
33
Accuracy spec: 2 K
Precision spec: 6.5 K
number: 1561
bias: -0.46 K
std: 1.96 K
number: 876
bias: -0.33 K
std: 2.00 K
number: 356
bias: -0.23 K
std: 1.89 K
PASSED
July August September

## Slide 34: PLPT ABI-FD-DSI:
2022.07-2022.09
CAPE vs RAOB
34
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
number: 808
bias: -217.72 J/kg
std: 342.25 J/kg
number: 462
bias: -195.84 J/kg
std: 363.75 J/kg
number: 124
bias: -146.67 J/kg
std: 201.27 J/kg
PASSED
July August September

## Slide 35: PLPT ABI-FD-DSI:
2022.07-2022.09
SI vs RAOB
35
Accuracy spec: 2 K
Precision spec: 6.5 K
number: 1405
bias: 0.32 K
std: 2.22 K
number: 809
bias: 0.25 K
std: 2.11 K
number: 326
bias: 0.22 K
std: 2.19 K
PASSED
July August September

## Slide 36: PLPT ABI-FD-DSI:
2022.07-2022.09
KI vs RAOB
36
Accuracy spec: 2 K
Precision spec: 5 K
number: 1405
bias: 0.41 K
std: 6.94 K
number: 809
bias: 0.20 K
std: 6.65 K
number: 326
bias: 1.24 K
std: 8.30 K
July August September

## Slide 37: PLPT ABI-FD-DSI:
2022.07-2022.09
TT vs RAOB
37
Accuracy spec: 1 K
Precision spec: 4 K
number: 1405
bias: -0.72 K
std: 3.97 K
number: 809
bias: -0.87 K
std: 3.73 K
number: 326
bias: -0.44 K
std: 4.36 K
July August September

## Slide 38: PLPT ABI-CONUS-DSI:
38
Accuracy spec: 2 K
Precision spec: 6.5 K
2022.07-2022.09
LI vs RAOB
number: 689
bias: -0.47 K
std: 1.97 K
number: 373
bias: -0.50 K
std: 2.09 K
number: 143
bias: -0.26 K
std: 1.58 K
PASSED
July August September

## Slide 39: PLPT ABI-CONUS-DSI:
2022.07-2022.09
CAPE vs RAOB
39
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
number: 176
bias: -93.73 J/kg
std: 216.51 J/kg
number: 109
bias: -103.70 J/kg
std: 252.88 J/kg
number: 30
bias: -66.93 J/kg
std: 153.94 J/kg
PASSED
July August September

## Slide 40: PLPT ABI-CONUS-DSI:
2022.07-2022.09
SI vs RAOB
40
Accuracy spec: 2 K
Precision spec: 6.5 K
number: 553
bias: -0.09 K
std: 2.30 K
number: 320
bias: 0.03 K
std: 2.22 K
number: 118
bias: -0.09 K
std: 2.04 K
PASSED
July August September

## Slide 41: PLPT ABI-CONUS-DSI:
2022.07-2022.09
KI vs RAOB
41
Accuracy spec: 2 K
Precision spec: 5 K
number: 553
bias: 0.92 K
std: 7.55 K
number: 320
bias: 0.08 K
std: 7.08 K
number: 118
bias: 1.07 K
std: 8.09 K
July August September

## Slide 42: PLPT ABI-CONUS-DSI:
2022.07-2022.09
TT vs RAOB
42
Accuracy spec: 1 K
Precision spec: 4 K
number: 553
bias: -0.53 K
std: 4.92 K
number: 320
bias: -0.84 K
std: 4.46 K
number: 118
bias: -0.76 K
std: 4.75 K
July August September

## Slide 43: PLPT ABI-MESO1-DSI:
43
Accuracy spec: 2 K
Precision spec: 6.5 K
2022.07-2022.09
LI vs RAOB
number: 87
bias: -0.85 K
std: 2.34 K
number: 104
bias: -0.82 K
std: 2.33 K
number: 182
bias: -0.70 K
std: 1.69 K
PASSED
July August September

## Slide 44: PLPT ABI-MESO1-DSI:
2022.07-2022.09
CAPE vs RAOB
44
Accuracy spec: 1000 J/kg
Precision spec: 2500 J/kg
number: 10
bias: -64.74 J/kg
std: 84.99 J/kg
number: 22
bias: -68.87 J/kg
std: 101.97 J/kg
number: 20
bias: -15.78 J/kg
std: 112.49 J/kg
PASSED
July August September

## Slide 45: PLPT ABI-MESO1-DSI:
2022.07-2022.09
SI vs RAOB
45
Accuracy spec: 2 K
Precision spec: 6.5 K
number: 68
bias: -0.63 K
std: 2.41 K
number: 84
bias: 0.52 K
std: 2.11 K
number: 143
bias: -0.59 K
std: 1.77 K
PASSED
July August September

## Slide 46: PLPT ABI-MESO1-DSI:
2022.07-2022.09
KI vs RAOB
46
Accuracy spec: 2 K
Precision spec: 5 K
number: 68
bias: 2.81 K
std: 8.39 K
number: 84
bias: 0.59 K
std: 7.50 K
number: 143
bias: 1.36 K
std: 6.29 K
July August September

## Slide 47: PLPT ABI-MESO1-DSI:
2022.07-2022.09
TT vs RAOB
47
Accuracy spec: 1 K
Precision spec: 4 K
number: 68
bias: 0.44 K
std: 5.14 K
number: 84
bias: -0.06 K
std: 5.03 K
number: 143
bias: 0.14 K
std: 4.42 K
July August September

## Slide 48: DSI Performance Summary
DSI retrieval is working as expected on GOES-18 ABI data when combined with NWP short-range forecasts (as first guess);
With a highly quantitative web-based tool (http://soundingval.ssec.wisc.edu) and the comparisons with RAOB, it indicates the performances from LI, CAPE and SI meet spec. for all the coverages, but the comparisons of TT and KI with RAOBs show the values are higher, particularly for the precision.
48

## Slide 49: GOES-16 vs. GOES-18 ABI LAP Products comparisons
Clear-sky, Overlapped coverage
GOES 16
GOES 18
GOES 18 – GOES 16
Temp at 850 mb
2022.09.15 00Z

## Slide 50
GOES-18 vs. GOES-16 comparisons
LVT and LVM
Bias and STD for the overlapped area (zenith angle ≤ 65)
LVTT
LVMM
N = 133,237
N = 133,237
2022.09.15 00Z

## Slide 51
GOES-18 vs. GOES-16 comparisons
TPW and DSI
2022.09.15 00Z
LVMP
N = 92710
TPW
LI
CAPE
SI
KI
TT
G18 – G16 statistics (zenith angle ≤ 65)
GOES 17

## Slide 52: GOES-17 vs. GOES-18 ABI LAP Products comparisons
Clear-sky, Overlapped coverage
GOES 17
GOES 18
GOES 18 – GOES 17
RH at 850 mb
2022.10.05 00Z

## Slide 53
GOES-18 vs. GOES-17 comparisons
LVT and LVM
Bias and STD for the overlapped area (zenith angle ≤ 65)
LVT
LVM
N = 133,237
N = 133,237
2022.10.05 00Z

## Slide 54
GOES-18 vs. GOES-17 comparisons
TPW and DSI
2022.10.05 00Z
N = 375725
TPW
LI
CAPE
SI
KI
TT
G18 – G17 statistics (zenith angle ≤ 65)
GOES 17

## Slide 55: PLPT Outcomes: Summary
All PLPT activities needed to make LAP products provisional have been completed
  Similar to GOES-16 performance
Minor issues revealed by PLPTs:
  Missing values in random boxed areas
  Slightly large discrepancy of some DSI products (KI and TT) compared with RAOB
These minor issues may not prevent the declaration of Provisional Maturity

## Slide 56: Path to Full Maturity Review

## Slide 57: Path to Full Maturity Review
We expect to apply the same PLPTs to be conducted for Full Maturity
  Extend period for testing starting July 2022 and beyond.
  Save L2 to enable further comparisons with the reference datasets.
  Deep dive for those small samples that have large differences between LAP and references.
Currently minor issues may not prevent declaration of Full Maturity (3 issues identified through the PLPT work and will be mitigated during provisional stage)
  Missing values are randomly discovered over some boxed areas.
  LAP products are affected by the migration of the sun which might be caused by the cloud mask.
  TT and KI values have slightly large discrepancy when compared with (“point-source”) RAOBs; previous experiences show that the results are closer to specification when considering only unstable atmospheric conditions.

## Slide 58: Issue #1 – Missing data over randomly distributed boxed areas
Initial analysis showed missing data over randomly distributed boxed area
  The missing data occur frequently and randomly in boxed shapes
Need to submit an ADR on this issue
  This issue was raised for GOES-17, also happens for GOES-16, and it is not solved.
Notes: PRO team may clarify more about this.

## Slide 59: An example of the missing data in boxed area over Full disk
Data missing occur randomly, but often between 8:20 and 9:40 UTC

## Slide 60: Missing data for M4 mode (5 minutes full disk)
At September 25, 2022, M4 scan mode was tested, in which the full disk scan is at every 5 minutes from 1700 UTC to 2100 UTC.
  The complete 5 minutes L2 sounding data is only available from 1500 UTC to 1720 UTC
  The missing data box is found at 1725 UTC
  All data are missing from 1730 UTC to 21 UTC.
1720 UTC
1725 UTC
1730 UTC
Notes: PRO team may clarify more about this.

## Slide 61: Issue #2 – Weak effects of sun migration on products
Notes: PRO team may clarify more about this.

## Slide 62: Risks to Reaching Full
Risk Name | Description | Impact | Mitigation and Schedule
Missing values over randomly distributed areas | Infrequently, there are missing values over randomly distributed boxed areas, but just the full disk sector. | Minor | Suggest an ADR, similar to an earlier one which we thought was resolved.
The migration of the sun affecting the LAP products | The ABI LAP products are affected by sun-rise and sun-set. | Minor | Cloud mask may have influences on the ABI LAP products, as the scenes are illuminated, although appears to be a yield issue.
Wet bias of the relative humidity in upper troposphere (100 - 300 hPa) | The relative humidity in upper troposphere (100-300 hPa) shows large wetter bias than the spec. | Minor | Radiosonde has dry bias in observing the relative humidity in the upper troposphere. Does not pose risk for full maturity.
Slightly large discrepancy of several DSI | Several DSI show slightly larger discrepancy than the spec, compared to radiosondes. | Minor | If the atmospheric conditions are unstable, the statistics results are closer to the requirements. May need a high spectrally resolution sounder in geo to fully resolve.
Small Impact
Moderate Impact
Large Impact

## Slide 63: Other concerns to Full Maturity
Layered PW (LPW) should be considered in the intermediate products based on the feedback from forecasters during Hazardous Weather Testbed (HWT) demonstration. LPW is available in IP from GOES-16.
Notes: HWT – Hazardous Weather Testbed

## Slide 64: SUMMARY AND RECOMMENDATIONS
GOES-18 ABI L2 LAP Product Provisional PS-PVR

## Slide 65: Provisional Validation
Preparation Activities | Assessment
Validation activities are ongoing and the general research community is now encouraged to participate. | true
Severe algorithm anomalies are identified and under analysis. Solutions to anomalies are in development and testing. | no severe anomalies detected
Incremental product improvements may still be occurring. | true
L2+ only: Users are engaged in the Product Feedback Forums and user feedback is assessed. | ongoing
End State | Assessment
Product performance has been demonstrated through analysis of a small number of independent measurements obtained from select locations, periods, and associated ground truth or field campaign efforts. | true
Product analysis is sufficient to communicate product performance to users relative to expectations (Performance Baseline). | true
Documentation of product performance exists that includes recommended remediation strategies for all anomalies and weaknesses. Any algorithm changes associated with severe anomalies have been documented, implemented, tested, and shared with the user community. | ongoing
Testing has been fully documented. | ongoing
Product is ready for operational use and for use in comprehensive cal/val activities and product optimization. | true

## Slide 66: Summary
A webpage has been developed for GOES-18 LAP product validation in near real-time
AWG LAP team has validated GOES-18 LAP products (TPW, LVT, LVM, DSI) from July 2022 to September 2022 with various reference data (RAOB, Suomi-Net GPS, AMSR2), the performance overall meet the requirements ;
AWG LAP team recommend that TPW, LVT, LVM, and DSI products be transitioned to Provisional status at this time;
AWG LAP team have found the following minor issues which should not prevent Provisional status
  Missing values occur frequently and randomly over boxed areas.
  The migration of the sun affects the LAP products via cloud mask.
  Comparisons of TT and KI with RAOBs shows a little larger than spec.

## Slide 67: Backup Material
GOES-18 ABI L2 LAP Product Provisional PS-PVR