## Slide 1: GOES-19 ABI L2+ SW Radiation Budget (SRB) Provisional PS-PVR
March 12, 2025
GOES-R AWG
Istvan Laszlo1, Hye-Yun Kim2, Hongqing Liu2, Rachel Pinker3, Kathy Lantz4 and the PRO Team
1NOAA/NESDIS/STAR, 2STC, 3University of Maryland, 4NOAA/OAR/ESRL

## Slide 2: Outline
Product Overview
Review of ADRs
Provisional Maturity Assessment
  Comparison with other satellite and reference data
Path to Full Validated Maturity
Summary and Recommendations

## Slide 3: Product Overview: RSR
Reflected Shortwave Radiation: Top-Of-Atmosphere
  instantaneous SW (0.2-4.0 µm) flux emerging at the Earth’s TOA,
  produced at the 2-km ABI pixel resolution every 10 minutes for Full Disk.
    Enterprise Processing System (EPS) products.
  SRB Enterprise algorithm description is not yet available in Product Definition and User’s Guide (PUG).
 | Measurement |  |  |  | Mapping
Region | Range | Accuracy | Precision | Performance Conditions | Accuracy
Full Disk | 0 to 1300 W/m2 | 85 W/m2 at high end of range (>500 W/m2) 65 W/m2 at middle of range (200-500 W/m2) 110 W/m2 at low end of range (<200 W/m2)[2] | 100 W/m2 for high end of range (>500 W/m2) 130 W/m2 for middle of range (200-500 W/m2) 100 W/m2 for low end of range (<200 W/m2) | LZA ≤ 70 degrees, daytime [1] | Full Disk: 2 km
[1] Conditions for good quality prescribed by the algorithm are for SZA ≤ 70 degrees.
[2] Available at: https://www.star.nesdis.noaa.gov/goesr/documentation_ATBDs.php.
Table 2.5. in Algorithm Theoretical Basis Document for enterprise processing system version (09/28/20)[2]

## Slide 4: Product Overview: DSR
Downward Shortwave Radiation: Surface
  instantaneous SW (0.2-4.0 µm) flux received at the Earth’s surface,
  produced at the 2-km ABI pixel resolution every 10 minutes for Full Disk.
    Enterprise Processing System (EPS) products.
  SRB Enterprise algorithm description is not yet available in Product Definition and User’s Guide (PUG).
[1] Conditions for good quality prescribed by the algorithm are for SZA ≤ 70 degrees.
[2] Available at: https://www.star.nesdis.noaa.gov/goesr/documentation_ATBDs.php.
Table 2.1. in Algorithm Theoretical Basis Document for enterprise processing system version (09/28/20)[2]
 | Measurement |  |  |  | Mapping
Region | Range | Accuracy | Precision | Performance Conditions | Accuracy
Full Disk | 0 to 1500 W/m2 | 85 W/m2 at high end of range (>500 W/m2) 65 W/m2 at middle of range (200-500 W/m2) 110 W/m2 at low end of range (<200 W/m2)[2] | 100 W/m2 for high end of range (>500 W/m2) 130 W/m2 for middle of range (200-500 W/m2) 100 W/m2 for low end of range (<200 W/m2) | LZA ≤ 70 degrees, daytime [1] | Full Disk: 2 km

## Slide 5: Product Overview: PAR
Photosynthetically Active Radiation
  instantaneous visible (0.4-0.7 µm) flux received at the Earth’s surface,
  produced at the 2-km ABI pixel resolution (2 km) every 10 minutes for Full Disk.
    New product in Enterprise Processing System (EPS) and not yet available at AWS.
  SRB Enterprise algorithm description is not yet available in Product Definition and User’s Guide (PUG).
[1] Conditions for good quality prescribed by the algorithm are for SZA ≤ 70 degrees.
[2] Available at: https://www.star.nesdis.noaa.gov/goesr/documentation_ATBDs.php.
Table 2.3. in Algorithm Theoretical Basis Document for enterprise processing system version (09/28/20)[2]
 | Measurement |  |  |  | Mapping
Region | Range | Accuracy | Precision | Performance Conditions | Accuracy
Full Disk | 0 to 700 W/m2 | 55 W/m2 at high end of range (>250 W/m2) 45 W/m2 at middle of range (100-250 W/m2) 70 W/m2 at low end of range (<100 W/m2)[2] | 65 W/m2 for high end of range (>250 W/m2) 85 W/m2 for middle of range (100-250 W/m2) 65 W/m2 for low end of range (<100 W/m2) | LZA ≤ 70 degrees, daytime [1] | Full Disk: 2 km

## Slide 6: GOES-R DSR/RSR/PAR Product Precedence Chain
4-level Cloud Mask
Snow Mask
ABI FSC product
GFS water equivalent snow depth
TPW
ABI product
GFS product
Climatology
DSR
RSR
PAR
Cloud & Moisture Imagery
Indirect Path Algorithm
Cloud phase, optical depth, droplet size, top height
ABI
Climatology

## Slide 7: Pre-Provisional Time-Line
25 Jun 2024 GOES-U Launch
7 Jul 2024 Renamed GOES-19
18 Jul 2024 Reached test position at 89.5° W
1 Oct 2024 GOES-19 SRB Beta Maturity
20 Dec 2024 L1b data reached Provisional
29 Jan 2025 Clear-sky mask reached Provisional
12 Mar 2025 GOES-19 SRB PS-PVR Provisional

## Slide 8: ADRs IN PROGRESS PRIOR TO GOES-19 SRB PROVISIONAL REVIEW
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 9: ADRs in Progress
Title | Description (date submitted) | Impact | Mitigation | Status
ADR1489 | ClearInstAlb (time-series of clear sky instantaneous TOA albedo) is reset when ABI mode change from Mode 6 to Mode 4 or the other way (09/11/24) | Missing ClearCompAlb impacts flux retrieval quality. | TBD | In analysis
ADR1521 | Flux is retrieved in missing block/stripe in upstream input products or flux retrieval is not attempted when upstream input products have valid retrievals (11/07/24) | Incorrect retrieval hinders usage and getting information from it. | TBD | In analysis
Little Impact
Moderate Impact
Big Impact
ADRs apply to G16, G18 and G19.

## Slide 10: Product Quality Evaluation
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 11: Provisional PLPTs
B, P, F indicate test is required for Beta, Provisional, Full maturity.
* Evaluation of MESO product was attempted but ultimately not possible to perform during GOES-17/18 Provisional testing due to an incorrect mapping issue.
^ With implementation of the Enterprise version of the algorithm, the PAR product is added, and the MESO and CONUS products are decommissioned. RIMP/PLPT tests 02, 03, 05, 07 and 08 do not apply for GOES-19.
Reference: Geostationary Operational Environmental Satellite (GOES) – R Series ABI L2+ Surface Downward Shortwave Radiation and Top-of-Atmosphere Reflected Shortwave Radiation (DSR-RSR) Beta, Provisional and Full Validation Readiness, Implementation and Management Plan (RIMP) (v2.0; 410-R-RIMP-0327, Oct 6,2021).
Test ID | Short description | 16 | 17 | 18 | 19
ABI-FD_DSR01 ABI-FD_RSR01 ABI-FD_PAR01^ | Verify that Mode 6 FD products are within range | B | P | P | P
ABI-CONUS_DSR02 ABI-CONUS_RSR02 | Verify that Mode 6 CONUS products are within range | B | P | P^ | N/A
ABI-MESO_DSR03 | Verify that Mode 6 mesoscale products are within range | B | P* | N/A^ | N/A
ABI-FD_DSR04 ABI-FD_RSR04 ABI-FD_PAR04^ | Verify that Mode 4 FD products are within range | B | P | P | P
ABI-CONUS_DSR05 ABI-CONUS_RSR05 | Verify that Mode 4 CONUS products are within range | B | P | P^ | N/A
ABI-FD_DSR06 ABI-FD_RSR06 ABI-FD_PAR06^ | Assessment of FD accuracy and precision | B, P, F | P, F | P, F | P, F
ABI-CONUS_DSR07 ABI-CONUS_RSR07 | Assessment of CONUS accuracy and precision | B, P, F | P, F | P, F^ | N/A
ABI-MESO_DSR08 | Assessment of mesoscale accuracy and precision | B, P, F | P* | N/A^ | N/A

## Slide 12: Application of PLPT Analysis Tests to Domains
CERES: Clouds and the Earth Radiant Energy System
SURFRAD: Surface Radiation Budget Network (US)
SOLRAD: Solar radiation network (US)
Analysis Method |  | FD
Visual | Inspection for range | 
 | Comparison with GOES-16 | 
Quantitative | Comparison with GOES-16 | 
 | Comparison of GOES-19 DSR with ground measurements (SURFRAD and SOLRAD) | 
 | Comparison of GOES-19 PAR with ground measurements (SURFRAD) | 
 | Comparison of GOES-19 RSR with CERES RSR | 

## Slide 13: GOES-19 Data Used in this Review
G19 DSR, RSR, and PAR in FD.
Time period: 10/29/24 – 01/15/25
  G19 L1b reached Beta maturity on 10/01/24
    SRB algorithm requires 29-day of clear sky TOA albedo time-series
Matchups (set of quasi coincident and collocated G19 and reference data):
  RSR with CERES observations.
  DSR with SURFRAD and SOLRAD measurements.
    G19 data are spatially averaged within an area of 25-km radius centered on ground site.
    Reference data are temporally averaged within ±30-min centered on G19 retrieval time.
  PAR with SURFRAD measurements.
    Same as DSR

## Slide 14: G19/G16 FD DSR Comparison 18 UTC on 10/30/24
PLPT test ABI-FD_DSR01
G19 remapped to G16 position.
G19 and G16 Full Disk (FD) DSRs are visually similar.
G19 DSR is in expected range.
Distributions of good quality FD DSR from G19 and G16 are similar.

## Slide 15: G19/G16 FD RSR Comparison 18 UTC on 10/30/24
PLPT test ABI-FD_RSR01
G19 remapped to G16 position.
G19 and G16 Full Disk (FD) RSRs are visually similar.
G19 RSR is in expected range.
Distributions of good quality FD RSR from G19 and G16 are similar.

## Slide 16: G19/G16 FD PAR Comparison 18 UTC on 10/30/24
PLPT test ABI-FD_PAR01
G19 remapped to G16 position.
G19 and G16 Full Disk (FD) PARs are visually similar.
G19 PAR is in expected range.
Distributions of good quality FD PAR from G19 and G16 are similar.

## Slide 17: G19 M4 16:35 UTC on 10/30/24
PLPT tests ABI-FD_DSR04, _RSR04, and _PAR04
G19 M4 Full Disk (FD) DSR, RSR, and PAR are in expected range.
Distributions of good quality fluxes from M4 FD shown in the histograms are similar to those from M6 FD.

## Slide 18: Summary of PLPT tasks 01 and 04
Tasks ABI-FD_DSR01, ABI-FD_RSR01, ABI-FD_PAR01:
  G19 FD M6 DSR, RSR, and PAR are within required measurement range.
  G19 and G16 FD DSRs, RSRs and PARs are visually similar.
Tasks ABI-FD_DSR04, ABI-FD_RSR04, ABI-FD_PAR04 :
  G19 FD M4 DSR, RSR, and PAR are within required measurement range.
  Distributions of M4 FD DSR, RSR, and PAR are similar to those from M6 FD.

## Slide 19: Comparison with Reference data
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 20: Definitions of Metrics for Quantitative Comparisons
Passed: Accuracy and Precision meet or slightly exceed requirements. Potential contributors for deviations are identified.
Partial-Passed: Accuracy/Precision deviates significantly from requirements, but potential contributors for deviations are identified.
Failed: Accuracy/Precision deviates significantly from requirements and source of poor performance is unknown, or source known and correction requires new algorithm.

## Slide 21: Comparison of GOES-19 RSR with CERES RSR
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 22: PLPT Task ABI-FD_RSR06
Comparison of G19 RSR with CERES/NOAA20 TOA reflected flux on 11/28/2024 over full disk:
  G19 (left), CERES (middle), and G19 – CERES difference (right).
  Largest differences (± 300 Wm-2) are over clouds and near the terminator. ABI “sees” clouds near the terminator where CERES does not, which causes overestimation.

## Slide 23: PLPT Task ABI-FD_RSR06
Comparison of G19 FD RSR product with CERES/NOAA20 TOA fluxes for 11/28/2024 over full disk.
Requirements are in parenthesis. Units: W m-2.
Only one day, but large N!
Accuracy (A) and precision (P) are within specs.
    Overestimation in low RSR range is from difference in scene types between ABI and CERES near the ABI terminator.
Accuracy (A): mean bias (satellite – reference)
Precision (P): standard deviation of biases
Number (N): number of samples
Range | A | P | N
CERES < 200 | 24 (110) | 59 (100) | 1,031,686
[200, 500] | 11 (65) | 71 (130) | 790,462
CERES > 500 | -16 (85) | 71 (100) | 163,391

## Slide 24: PLPT Task ABI-FD_RSR06
Comparison of G16 RSR with CERES/NOAA20 TOA reflected flux on 11/28/2024 over full disk:
  G16 (left), CERES (middle), and G16 – CERES difference (right).
  Largest differences (± 300 Wm-2) are over clouds and near terminator. ABI “sees” clouds near terminator where CERES does not.
  Similar to G19 RSR error patterns

## Slide 25: PLPT Task ABI-FD_RSR06
Comparison of G16 FD RSR product with CERES/NOAA20 TOA fluxes for 11/28/2024 over full disk.
Requirements are in parenthesis. Units: W m-2.
Accuracy (A) and precision (P) are similar to G19.
Overestimation in low RSR range is from difference in scene types between ABI and CERES near the ABI terminator.
Accuracy (A): mean bias (satellite – reference)
Precision (P): standard deviation of biases
Number (N): number of samples
Range | A | P | N
CERES < 200 | 29 (110) | 61 (100) | 972,855
[200, 500] | 20 (65) | 71 (130) | 822,824
CERES > 500 | -4 (85) | 73 (100) | 158,981

## Slide 26: PLPT Task ABI-FD_RSR06
Comparison of G19 FD RSR product with CERES/NOAA20 TOA fluxes for the time period 10/29/2024 – 01/15/2025 over ground stations.
  Number of samples (N) are smaller compared to full disk comparison.
Accuracy (A) and precision (P) are within specs.
G19 A&P statistics are similar to G16 A&P statistics.
Requirements are in parenthesis. Units: W m-2.
Accuracy (A): mean bias (satellite – reference)
Precision (P): standard deviation of biases
Number (N): number of samples
G19 |  |  | 
Range | A | P | N
CERES < 200 | 3 (110) | 44 (100) | 3551
[200, 500] | -14 (65) | 40 (130) | 3378
CERES > 500 | -38 (85) | 34 (100) | 24
G16 |  |  | 
Range | A | P | N
CERES < 200 | 3 (110) | 28 (100) | 3707
[200, 500] | -3 (65) | 41 (130) | 3569
CERES > 500 | -16 (85) | 32 (100) | 25

## Slide 27: Comparison of GOES-19 DSR with SURFRAD and SOLRAD DSR
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 28: Reference Data for Quantitative Evaluation of DSR
Surface Radiation Network (SURFRAD)
  Accurate, long-term, continuous measurements.
  7 permanent sites in climatologically diverse regions in the US.
Integrated Surface Irradiance Study (SOLRAD)
  Monitors surface radiation in the US, in collaboration with SURFRAD.
  7 stations are available.

## Slide 29: PLPT Task ABI-FD_DSR06
Comparison of FD DSR product with SURFRAD and SOLRAD for 10/29/2024 – 01/15/2025.
Requirements are in parenthesis. Units: W m-2.
Range | A | P | N
Ground < 200 | 18 (110) | 42 (100) | 34,153
[200, 500] | -1 (65) | 51 (130) | 22,727
Ground > 500 | -3 (85) | 37 (100) | 5,655
Accuracy (A) and Precision (P) requirements are met in all ranges.
Accuracy (A): mean bias (satellite – reference)
Precision (P): standard deviation of biases
Number (N): number of samples

## Slide 30: G19 and G16 DSR comparison over the same ground stations
DSR from G19 and G16 for 10/29/2024 – 01/15/ 2025 compared with ground measurements.
  G19 A and P are comparable to G16 A and P.
Dotted horizontal lines represent requirements.

## Slide 31: Comparison of GOES-19 PAR with SURFRAD PAR
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 32: PLPT Task ABI-FD_PAR06
Comparison of FD PAR product with SURFRAD for 10/29/2024 – 01/15/2025.
Requirements are in parenthesis. Units: W m-2.
Range | A | P | N
Ground < 100 | -1 (70) | 18 (65) | 17025
[100, 250] | -27 (45) | 21 (85) | 11333
Ground > 250 | -38 (55) | 14 (65) | 754
Accuracy (A) and Precision (P) requirements are met in all ranges.
Accuracy (A): mean bias (satellite – reference)
Precision (P): standard deviation of biases
Number (N): number of samples

## Slide 33: G19 and G16 PAR comparison over the same ground stations
PAR from G19 and G16 for 10/29/2024 – 01/15/ 2025 compared with ground measurements.
  G19 A and P are comparable to G16 A and P.
Dotted lines represent requirements.

## Slide 34: Summary of G19 vs. Reference RSR, DSR, and PAR Comparison
G19 RSR is evaluated with CERES RSR (Passed).
  A and P are within specs for all ranges.
  Quality of G19 RSR is very similar to quality of G16 RSR.
G19 DSR is evaluated with SURFRAD and SOLRAD ground data (Passed).
  A and P are within specs in ~ 2.5-month data.
  Quality of G19 DSR is very similar to quality of G16 DSR.
G19 PAR is evaluated with SURFRAD ground data (Passed).
  A and P are within specs in ~ 2.5-month data.
  Quality of G19 DSR is very similar to quality of G16 DSR.

## Slide 35: Provisional Maturity Assessment
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 36: Provisional Validation
Preparation Activities | Assessment
Validation activities are ongoing and the general research community is now encouraged to participate. | Validation activities are ongoing.
Severe algorithm anomalies are identified and under analysis. Solutions to anomalies are in development and testing. | No severe anomalies identified.
Incremental product improvements may still be occurring. | Incremental product improvements are expected.
Users are engaged in the Product Feedback Forums and user feedback is assessed | No feedback from users yet.

## Slide 37: Provisional Validation
End State | Assessment
Product performance has been demonstrated through analysis of a small number of independent measurements obtained from select locations, periods, and associated ground truth or field campaign efforts. | This has been demonstrated using CERES, SURFRAD and SOLRAD as truth and independent statellite retrivals from GOES-16 and GOES-18.
Product analysis is sufficient to communicate product performance to users relative to expectations (Performance Baseline). | Concur.
Documentation of product performance exists that includes recommended remediation strategies for all anomalies and weaknesses. Any algorithm changes associated with severe anomalies have been documented, implemented, tested, and shared with the user community. | These are documented in this PS-PVR presentation and will be documented in a separate ReadMe file.
Testing has been fully documented. | Concur (in PS-PVR slides).
Product is ready for operational use and for use in comprehensive cal/val activities and product optimization. | Concur.

## Slide 38: Path to full Validation Maturity
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 39: Issues and Status ADRs Potentially Needing Resolution for Full VAL
ADR | Title | Status | Build
1489 | ClearInstAlb reset when ABI mode changes | In analysis | --
1521 | Occasional blocks of missing retrievals | In analysis | --

## Slide 40: Issues and Status Other Actions Needed for Full VAL
The Enterprise algorithm uses empirical narrow-to-broadband conversions, but currently that is derived from G16 ABI data. It needs to be derived from G19 ABI data, which will need to be established for a long record (several month of data).
Action | Title | Desired Implementation Date into OE
N/A | L2 SRB algorithm - update the narrow-to-broadband (NTB) albedo conversion for G19 ABI | ≧6 month prior to PS-PVR FULL

## Slide 41: Path to Full Validation - PLPTs
AWG SRB Team will conduct these tests to further evaluate the L2 SRB product quality.
Full description of test plans and procedures are given in the Geostationary Operational Environmental Satellite (GOES)-R Series ABI L2+ Surface Downward Shortwave Radiation and Top-of-Atmosphere Reflected Shortwave Radiation (DSR-RSR) Beta, Provisional and Full Validation Readiness, Implementation and Management Plan (RIMP) (v2.0; 410-R-RIMP-0327, Oct 6,2021).
PLPT ID | Descriptive Title
ABI-FD_DSR06 ABI-FD_RSR06 ABI-FD_PAR06^ | Assess precision and accuracy of FD product for an extended period that includes seasonally representative number of independent measurements
^ With implementation of the Enterprise version of the algorithm, the PAR product is added.

## Slide 42: Path to Full Validation – Risks
Risk Name | Description | Impact | Mitigation and Schedule
Update NTB coefficients | as discussed; Priority 1 | Moderate | Extend G19 record used for developing empirical NTB; ≧6 month prior to PS-PVR FULL
Little Impact
Moderate Impact
Big Impact
NTB: narrowband-to-broadband

## Slide 43: Summary & Recommendations
GOES-19 Shortwave Radiation Budget L2 Product Provisional PS-PVR

## Slide 44: Summary
Measured FD DSR, RSR, and PAR performance against reference data
  Accuracy and precision specs are met in all ranges of DSR, RSR, and PAR.
  Updates will be needed for the narrow-to-broadband (NTB) transformation to further improve performance. Requires collection of more GOES-19 ABI and CERES data.
Overall, the GOES-19 FD DSR, RSR, and PAR products are ready for operational and scientific use
  In general, good quality retrievals are recommended for quantitative applications due to their better overall performance.

## Slide 45: Recommendation
AWG SRB Team believes that the GOES-19 L2 DSR, RSR and PAR Full Disk products have reached Provisional Maturity, as defined by the GOES-R Program.